PV Sysem Components:

A photovoltaic system typically includes an array of photovoltaic modules, an inverter, a battery pack for storage, interconnection wiring, and optionally a solar tracking mechanism.

Solar Array: Made of PV modules, Solar panels are typically measured under STC (standard test conditions) or PTC (PVUSA test conditions), in watts. Typical panel ratings range from less than 100 watts to over 400 watts. The array rating consists of a summation of the panel ratings, in watts, kilowatts, or megawatts.

Battery: Common battery technologies used in today's PV systems include the valve regulated lead-acid battery– a modified version of the conventional lead–acid battery, nickel–cadmium and lithium-ion batteries.
PV systems with an integrated battery solution also need a charge controller, as the varying voltage and current from the solar array requires constant adjustment to prevent damage from overcharging. Basic charge controllers may simply turn the PV panels on and off, or may meter out pulses of energy as needed, a strategy called PWM or pulse-width modulation.

Inverter: Systems designed to deliver alternating current (AC), such as grid-connected applications need an inverter to convert the direct current (DC) from the solar modules to AC.

Utility Meter: utility power is automatically provided at night and during the day when the demand exceeds your solar electric power production.

The utility meter actually spins backwards when solar power production exceeds house demand, allowing you to credit any excess electricity against future utility bills.

Terms:

Tilt Angle: PV Modules inclination, varies based on the lat.
Standard tAngle = lat – 15°

Isolation: Gathered energy in a day on an orizontally placed module. Measured in Kwh/sm

PV Panel: Made of PV modules. 8-10sm panel produces 1 Kwp D.C.

Solar K: 1.353 W/sm.

Irradiation: KW/sm. 1 KW/sm @ 12AM

PV Module Yield: Irradiation Energy/Obtained Energy. Typical yields: 4%-18%

Watt peak (Wp): Peak power while in standard conditions

Data Units:

Array voltage	VDC	V
Grid voltage	VAC	V
Array current	IDC	A
Grid current	IAC	A
Array power	PDC	W
Grid power	PAC	W

Module temperature	Tmod	°C
Ambient temperature	Tamb	°C
Global irradiance	G	W/m2
Global irradiation	H	J/m2
Wind speed	v	m/s

Inverter Efficiency:

Useful links:

http://www.3e.eu/monitoring-of-photovoltaic-systems-good-practices-and-systematic-analysis/
http://www.pvresources.com/en/inverters/monitoring.php